## Slide 1: Digital Logic Design I CS1026
Paula.Roberts@scss.tcd.ie

## Slide 2
The position of each digit in a weighted number system is assigned a weight based on the base or radix of the system. The radix of decimal numbers is ten, because only ten symbols (0 through 9) are used to represent any number. The column weights of decimal numbers are powers of ten that increase from right to left beginning with 100 =1:…105 104 103 102 101 100. For fractional decimal numbers, the column weights are negative powers of ten that decrease from left to right:
102 101 100. 10-1 10-2 10-3 10-4 …
NUMBER SYSTEMS

## Slide 3
Decimal Numbers
Express the number 480.52 as the sum of values of each digit.
Example
Solution
(9 x 103) + (2 x 102) + (4 x 101) + (0 x 100)
or
9 x 1,000 + 2 x 100 + 4 x 10 + 0 x 1
Decimal numbers can be expressed as the sum of the products of each digit times the column value for that digit. Thus, the number 9240 can be expressed as
480.52 = (4 x 102) + (8 x 101) + (0 x 100) + (5 x 10-1) +(2 x 10-2)

## Slide 4
For digital systems, the binary number system is used. Binary has a radix of two an d uses the digits 0 and 1 to represent quantities.
The column weights of binary numbers are powers of two that increase from right to left beginning with 20 =1:
…25 24 23 22 21 20.
For fractional binary numbers, the column weights are negative powers of two that decrease from left to right:
22 21 20. 2-1 2-2 2-3 2-4 …

## Slide 5
Binary Numbers
A binary counting sequence for numbers from zero to fifteen is shown.
0 0 0 0 0
1 0 0 0 1
2 0 0 1 0
3 0 0 1 1
4 0 1 0 0
5 0 1 0 1
6 0 1 1 0
7 0 1 1 1
8 1 0 0 0
9 1 0 0 1
10 1 0 1 0
11 1 0 1 1
12 1 1 0 0
13 1 1 0 1
14 1 1 1 0
15 1 1 1 1
Decimal Number
Binary Number
Notice the pattern of zeros and ones in each column.
Digital counters frequently have this same pattern of digits:

## Slide 6
Binary Conversions
The decimal equivalent of a binary number can be determined by adding the column values of all of the bits that are 1 and discarding all of the bits that are 0.
Convert the binary number 100101.01 to decimal.
Example
Solution
Start by writing the column weights; then add the weights that correspond to each 1 in the number.
25 24 23 22 21 20. 2-1 2-2
32 16 8 4 2 1 . ½ ¼
1 0 0 1 0 1. 0 1
32 +4 +1 +¼ =
37¼

## Slide 7
Binary Conversions
You can convert a decimal whole number to binary by reversing the procedure. Write the decimal weight of each column and place 1’s in the columns that sum to the decimal number.
Convert the decimal number 49 to binary.
Example
Solution
The column weights double in each position to the right. Write down column weights until the last number is larger than the one you want to convert.
26 25 24 23 22 21 20.
64 32 16 8 4 2 1.
0 1 1 0 0 0 1.

## Slide 8
You can convert a decimal fraction to binary by repeatedly multiplying the fractional results of successive multiplications by 2. The carries form the binary number.
Convert the decimal fraction 0.188 to binary by repeatedly multiplying the fractional results by 2.
Example
Solution
0.188 x 2 = 0.376 carry = 0
0.376 x 2 = 0.752 carry = 0
0.752 x 2 = 1.504 carry = 1
0.504 x 2 = 1.008 carry = 1
0.008 x 2 = 0.016 carry = 0
Answer = .00110 (for five significant digits)
MSB
Binary Conversions

## Slide 9
1
0
0
1
1
0
You can convert decimal to any other base by repeatedly dividing by the base. For binary, repeatedly divide by 2:
Convert the decimal number 49 to binary by repeatedly dividing by 2.
Example
Solution
You can do this by “reverse division” and the answer will read from left to right. Put quotients to the left and remainders on top.
49 2
Decimal number
base
24
remainder
Quotient
12
6
3
1
0
Continue until the last quotient is 0
Answer:
Binary Conversions

## Slide 10
Binary Addition
The rules for binary addition are
0 + 0 = 0 Sum = 0, carry = 0
0 + 1 = 1 Sum = 1, carry = 0
1 + 0 = 1 Sum = 1, carry = 0
1 + 1 = 10 Sum = 0, carry = 1
When an input carry = 1 due to a previous result, the rules are
1 + 0 + 0 = 01 Sum = 1, carry = 0
1 + 0 + 1 = 10 Sum = 0, carry = 1
1 + 1 + 0 = 10 Sum = 0, carry = 1
1 + 1 + 1 = 11 Sum = 1, carry = 1

## Slide 11
Binary Addition
Add the binary numbers 00111 and 10101 and show the equivalent decimal addition.
Example
Solution
00111 7
10101 21
0
1
0
1
1
1
1
0
1
28
=

## Slide 12
Binary Subtraction
The rules for binary subtraction are
0 - 0 = 0
1 - 1 = 0
1 - 0 = 1
10 - 1 = 1 with a borrow of 1
Subtract the binary number 00111 from 10101 and show the equivalent decimal subtraction.
Example
Solution
00111 7
10101 21
0
/1
1
1
1
0
14
/1
/1
=

## Slide 13
1’s Complement
The 1’s complement of a binary number is just the inverse of the digits. To form the 1’s complement, change all 0’s to 1’s and all 1’s to 0’s.
For example, the 1’s complement of 11001010 is
00110101
In digital circuits, the 1’s complement is formed by using inverters:
1 1 0 0 1 0 1 0
0 0 1 1 0 1 0 1

## Slide 14
2’s Complement
The 2’s complement of a binary number is found by adding 1 to the LSB of the 1’s complement.
Recall that the 1’s complement of 11001010 is
00110101 (1’s complement)
To form the 2’s complement, add 1:
+1
00110110 (2’s complement)
1 1 0 0 1 0 1 0
0 0 1 1 0 1 0 1
1
0 0 1 1 0 1 1 0

## Slide 15
Signed Binary Numbers
There are several ways to represent signed binary numbers. In all cases, the MSB in a signed number is the sign bit, that tells you if the number is positive or negative.
Computers use a modified 2’s complement for signed numbers. Positive numbers are stored in true form (with a 0 for the sign bit) and negative numbers are stored in complement form (with a 1 for the sign bit).
For example, the positive number 58 is written using 8-bits as 00111010 (true form).
Sign bit
Magnitude bits

## Slide 16
Signed Binary Numbers
Assuming that the sign bit = -128, show that 11000110 = -58 as a 2’s complement signed number:
Example
Solution
1 1 0 0 0 1 1 0
Column weights: -128 64 32 16 8 4 2 1.
-128 +64 +4 +2 = -58
Negative numbers are written as the 2’s complement of the corresponding positive number.
-58 = 11000110 (complement form)
Sign bit
Magnitude bits
An easy way to read a signed number that uses this notation is to assign the sign bit a column weight of -128 (for an 8-bit number). Then add the column weights for the 1’s.
The negative number -58 is written as:

## Slide 17
Floating Point Binary Numbers
The binary point is understood to be left of the 23 bit mantissa.
Effectively there are 24 bits in the mantissa as the MSB is always a 1. This 1 is understood to be there but does not occupy an actual bit position.
The biased exponent is obtained by adding 127 to the actual exponent. The bias allows you to express very small or big number without requiring a sign bit for the exponent. Actual exponent values are from -126 to +128
Floating point notation is capable of representing very large or small numbers by using a form of scientific notation. A 32-bit single precision number is illustrated below.
The sign bit represents the sign of the number
The Mantissa represents the magnitude of the number and is between 0 and 1.
The Exponent represents the number of paces that the (decimal or binary) point must be moved,.
S E (8 bits) F (23 bits)
Sign bit
Magnitude with MSB dropped
Biased exponent (+127)

## Slide 18
Single Precision Floating Point Binary Numbers
Example
Express 1011010010001 in floating point format
Move binary point 12 places to the left and multiply by appropriate power of 2
1011010010001 = 1.011010010001 x 2 12
S=0 since positive
Exponent =12 => biased exponent E =12+127 = 139 = 10001011
Mantissa = .011010010001 (note we ignore the 1) and pad to 23 bits with zeros
Solution
0 10001011
011010010001 00000000000
S E F

## Slide 19
Single Precision Floating Point Binary Numbers
Express the speed of light, c, in single precision floating point notation. (c = 0.2998 x 109)
Example
Solution
In scientific notation, c = 1.0001 1101 1110 1001 0101 1100 0000 x 228.
0 10011011 0001 1101 1110 1001 0101 110
Convert c to binary
In binary, c =10001 1101 1110 1001 0101 1100 0000
S = 0 because the number is positive. E = 28 + 127 = 15510 = 1001 10112. F is the next 23 bits after the first 1 is dropped.
In floating point notation, c =

## Slide 20
Arithmetic Operations with Signed Numbers
Using the signed number notation with negative numbers in 2’s complement form simplifies addition and subtraction of signed numbers. Rules for addition: Add the two signed numbers. Discard any final carries. The result is in signed form.
Examples:
00011110 = +30
00001111 = +15
00101101
= +45
00001110 = +14
11101111 = -17
11111101
= -3
11111111 = -1
11111000 = -8
11110111
= -9
1
Discard carry

## Slide 21
Arithmetic Operations with Signed Numbers
01000000 = +64
01000001 = +65
10000001
= -1
10000001 = -127
10000001 = -127
100000010
= +2
Note that if the number of bits required for the answer is exceeded, overflow will occur. This occurs only if both numbers have the same sign. The overflow will be indicated by an incorrect sign bit.
Two examples are:
Wrong! The answer is incorrect and the sign bit has changed.
Discard carry

## Slide 22
Arithmetic Operations with Signed Numbers
Rules for subtraction: 2’s complement the subtrahend and add the numbers. Discard any final carries. The result is in signed form. Repeat the examples done previously, but subtract:
00001111
= +15
1
Discard carry
2’s complement subtrahend and add:
00011110 = +30
11110001 = -15
00011110
00001111
-
00001110
11101111
11111111
11111000
-
-
00011111
= +31
00001110 = +14
00010001 = +17
00000111
= +7
1
Discard carry
11111111 = -1
00001000 = +8
(+30)
–(+15)
(+14)
–(-17)
(-1)
–(-8)

## Slide 23
Hexadecimal Numbers
Hexadecimal uses sixteen characters to represent numbers: the numbers 0 through 9 and the alphabetic characters A through F. Large binary number can easily be converted to hexadecimal by grouping bits 4 at a time and writing the equivalent hexadecimal character.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 8 9 A B C D E F
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Hexadecimal
Binary
Express 1001 0110 0000 11102 in hexadecimal:
Example
Solution
Group the binary number by 4-bits starting from the right. Thus, 960E

## Slide 24
Hexadecimal Numbers
Hexadecimal is a weighted number system. The column weights are powers of 16, which increase from right to left.
.
1 A 2 F16
670310
Column weights
163 162 161 160
4096 256 16 1
.
{
Express 1A2F16 in decimal.
Example
Solution
Start by writing the column weights:
4096 256 16 1
1(4096) + 10(256) +2(16) +15(1) =
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0 1 2 3 4 5 6 7 8 9 A B C D E F
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Hexadecimal
Binary

## Slide 25
BCD
Binary coded decimal (BCD) is a weighted code that is commonly used in digital systems when it is necessary to show decimal numbers such as in clock displays.
0 1 2 3 4 5 6 7 8 9 10 11 12 13 1415
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 1010 1011 1100 1101 1110 1111
Decimal
Binary
BCD
0001 0001 0001 0001 0001 0001
0000 0001 0010 0011 0100 0101 0110 0111 1000 1001 0000 0001 0010 0011 0100 0101
The table illustrates the difference between straight binary and BCD. BCD represents each decimal digit with a 4-bit code. Notice that the codes 1010 through 1111 are not used in BCD.

## Slide 26
BCD
You can think of BCD in terms of column weights in groups of four bits. For an 8-bit BCD number, the column weights are: 80 40 20 10 8 4 2 1.
Question:
What are the column weights for the BCD number 1000 0011 0101 1001?
Answer:
8000 4000 2000 1000 800 400 200 100 80 40 20 10 8 4 2 1
Note that you could add the column weights where there is a 1 to obtain the decimal number. For this case:
8000 + 200 +100 + 40 + 10 + 8 +1 = 835910

## Slide 27
ASCII
ASCII is a code for alphanumeric characters and control characters. In its original form, ASCII encoded 128 characters and symbols using 7-bits. The first 32 characters are control characters, that are based on obsolete teletype requirements, so these characters are generally assigned to other functions in modern usage. In 1981, IBM introduced extended ASCII, which is an 8-bit code and increased the character set to 256. Other extended sets (such as Unicode) have been introduced to handle characters in languages other than English.

## Slide 28
Parity Method
The parity method is a method of error detection for simple transmission errors involving one bit (or an odd number of bits). A parity bit is an “extra” bit attached to a group of bits to force the number of 1’s to be either even (even parity) or odd (odd parity).
The ASCII character for “a” is 1100001 and for “A” is 1000001. What is the correct bit to append to make both of these have odd parity?
Example
Solution
The ASCII “a” has an odd number of bits that are equal to 1; therefore the parity bit is 0. The ASCII “A” has an even number of bits that are equal to 1; therefore the parity bit is 1.

## Slide 29
Problems/ solutions
Convert the following binary numbers to decimal
(a) 11 = 1 × 21 + 1 × 20 = 2 + 1 = 3
(b) 100 = 1 × 22 + 0 × 21 + 0 × 20 = 4
(c) 111 = 1 × 22 + 1 × 21 + 1 × 20 = 4 + 2 + 1 = 7
(d) 1000 = 1 × 23 + 0 × 22 + 0 × 21 + 0 × 20 = 8
(e) 1001 = 1 × 23 + 0 × 22 + 0 × 21 + 1 × 20 = 8 + 1 = 9
(f) 1100 = 1 × 23 + 1 × 22 + 0 × 21 + 0 × 20 = 8 + 4 = 12
(g) 1011 = 1 × 23 + 0 × 22 + 1 × 21 + 1 × 20 = 8 + 2 + 1 = 11
(h) 1111 = 1 × 23 + 1 × 22 + 1 × 21 + 1 × 20 = 8 + 4 + 2 + 1 = 15
(a) 110011.11 = 1 × 25 + 1 × 24 + 1 × 21 + 1 × 20 + 1 × 2−1 + 1 × 2−2
= 32 + 16 + 2 + 1 + 0.5 + 0.25 = 51.75
(b) 101010.01 = 1 × 25 + 1 × 23 + 1 × 21 + 1 × 2−2 = 32 + 8 + 2 + 0.25
= 42.25
(c) 1000001.111 = 1 × 26 + 1 × 20 + 1 × 2−1 + 1 × 2−2 + 1 × 2−3
= 64 + 1 + 0.5 + 0.25 + 0.125 = 65.875
Convert the following binary numbers to decimal

## Slide 30
Convert the following to binary using the sum of weights method
Convert the following to binary by repeated division by 2
15, 21, 28
Problems/ solutions

## Slide 31
Add the following binary numbers
Subtract the following binary numbers
Problems/ solutions

## Slide 32
Determine the 2’s complement of the following
10, 111, 1001, 1101, 11100, 10011, 10110000, 00111101
Convert each pair of decimal numbers to binary and add using 2’s complement form
Problems/ solutions

## Slide 33
Convert these hex numbers to binary
Convert to BCD
Problems/ solutions

## Slide 34
Convert these BCD numbers to Decimal
Problems/ solutions

## Slide 35
Attach an even parity bit to the following bytes
Problems/ solutions